(Specifier Note:  The purpose of this guide specification is to assist the specifier in correctly specifying wood folding patio doors and their installation.  The specifier needs to edit these guide specifications to fit the needs of each specific project.  Contact a JELD-WEN® representative to assist in appropriate product selections.  Throughout the guide specification, there are Specifier Notes to assist in the editing of the file.

References have been made within the text of the specification to MasterFormat 2004 Section numbers and titles, specifier needs to coordinate these numbers and titles with sections included for the specific project.  Brackets []; “AND/OR”; and “OR” have been used to indicate when a selection is required.  Some options may require additional lead-time, if this is a consideration, contact a JELD-WEN® representative for assistance.)

SECTION 08 14 74.00 CUSTOM

WOOD EXTERIOR PATIO DOORS

JELD-WEN® Custom Wood Folding Patio Doors

GENERAL

SECTION INCLUDES

Wood Folding Patio Doors

Prehung Hardwood Systems

Glazing

SUBMITTALS

Refer to Section [01 33 00 Submittal Procedures]  [Insert section number and title].

Product Data: Submit door manufacturer current product literature, including installation instruction.

Samples: Provide finish samples for all products.

Quality Assurance Submittals

(Specifier Note:  DELETE Design Data, Test Reports submittal requirements when propriety specification is used and can be held.  MAINTAIN Design Data, Test Reports submittal requirement when other products may be submitted as substitution.)

Design Data:  Provide manufacturer test report numbers indicating product compliance with indicated requirements.

Manufacturer Instructions:  Provide manufacturer’s written installation instructions.

Closeout Submittals

Refer to Section [01 78 00 Closeout Submittals]  [Insert section number and title].

DELIVERY, STORAGE AND HANDLING

Refer to Section [01 60 00 Product Requirements] [Insert section number and title].

Deliver doors, materials and components in manufacturer’s original, unopened, undamaged containers with identification labels intact.

Store doors as recommended by manufacturer.

WARRANTY

Refer to Section [01 78 36 Warranties]  [Insert section number and title].

(Specifier Note:  DELETE warranty information not specific to project.)

Manufacturer standard warranty indicating that doors will be free from material and workmanship defects from the date of substantial completion for the time periods indicated below:

Insignia Door System:  5 Years.

AuraLast Wood Frames: Lifetime.

PRODUCTS

(Specifier Note: Product Information is proprietary to JELD-WEN®.  If additional products are required for competitive procurement, contact JELD-WEN® for assistance in listing competitive products that may be available.)

MANUFACTURER

JELD-WEN Windows and Doors; 3250 Lakeport Blvd. P.O. Box 1329; Klamath Falls, OR 97601-0268, USA; Phone 541.885.7412, fax 541.884.3331; Toll free 
800.535. 3936; website www.jeld-wen.com

(Specifier Note: Exterior wood doors can be customized in many ways including shape, size, design, carving, glass, transoms, casings, panels and moulding. INCLUDE the desired collection number for reference or DELETE design reference and describe properties of door in wood entrance doors article below. For more information or assistance in making appropriate product selections, contact a JELD-WEN® representative.)

Basis of Design:  Doors are based on the JELD-WEN®’s Custom Wood, Folding Patio Doors[, Design [509] [515]].

MATERIALS

(Specifier Note:  AuraLast™ is a trademark preservative treatment by JELD-WEN® and is distinguished from traditional preservation methods by its minimum treatment penetration of 92%.)

Wood: Western Pine, preservative treated with AuraLast™ in accordance with WDMA I.S.4.

WOOD FOLDING PATIO DOORS

Thickness: [1-3/8 inch] [1-3/4 inch] [2-1/4 inch].

Door Style: [Full Glass] [Paneled and Glass].

(Specifier Note: Edit paragraphs below to describe door or DELETE all and refer to Basis of Design.)

Shape: Squared.

Panel Profile:  [Convex Long] [Convex short] [V-Groove] [Double-Hip] [45 Degree] [Curved Radius] [1290 Panel] [1350/1355 Panel] [Flat].

Divided Lites: [Six] [Nine] [Ten] [Twelve] [Fifteen] [Mission].

Panel Mouldings: [Raised Moulding [112] [116] [141] [300] [800] [850] [1200]] [Ovolo 500] [Shaker (not raised)].

Wood Species and Finish

(Specifier Note: RETAIN one of six paragraphs below.)

(Specifier Note: Alder features a fairly straight grain with areas of burl clusters and a few small knots. These marks add character to the door and will provide darker texture and color when finished. Alder varies from pale yellow to reddish brown, and it accepts stains exceptionally well. It’s also the lightest and least dense of all the standard wood species offered.)

[Alder] [Knotty Alder] wood, with [Chappo] [Cherry] [Chesnut] [Clear] [Dark Cherry] [Ebony] [Gunstock] [Merlot] [Pebble Grey Mist] [Russet] [Wheat] [White Wash] Finish.

(Specifier Note: Cherry varies from rich red to reddish brown in color. It features a fine, straight and close grain with a smooth texture. Occasionally, thin gum pockets and small clusters of pin knots are visible. These character marks, along with random blonde streaks of sapwood, add a distinctive quality to the wood. Cherry stains easily and smoothly.)

Cherry wood, with [Chappo] [Cherry] [Chesnut] [Clear] [Dark Cherry] [Ebony] [Gunstock] [Merlot] [Russet] [Wheat] Finish.

(Specifier Note: Mahogany is the very best wood available. Its color ranges from reddish brown to a deep, rich red, and it stains well for a superior finish. The wood displays a prominent growth ring figure, with grain that is straight or interlocked. Mahogany offers less expansion, contraction and moisture absorption than most other hardwoods.)

Mahogany wood, with [Chappo] [Cherry] [Chesnut] [Dark Cherry] [Ebony] [Gunstock] [Merlot] [Russet] [Wheat] Finish.

(Specifier Note: Northern Red Oak ensures the greatest color and grain pattern consistency. Oak is renowned for its dramatically pronounced grain pattern. This pattern varies from a tight, vertical grain to a beautifully arched pattern. The color range includes light straw and honey with a light pink hue. It also accepts stains very well.)

Oak wood, with [Chappo] [Cherry] [Chesnut] [Clear] [Dark Cherry] [Ebony] [Gunstock] [Merlot] [Pebble Grey Mist] [Russet] [Wheat] [White Wash] Finish.

(Specifier Note: Walnut color varies from a rich, dark brown to black with purple undertones. Walnut features attractive blonde sapwood streaks within the darker tones, and it generally has a straight grain with occasional waves or curls.

[Knotty] Walnut wood, with [Chappo] [Clear] Finish.

Paint Surface

Color: [Ivory] [Swiss Coffee] [Eggshell] [Khaki] [Forest] [Cobalt] [Custom].

(Specifier Note: Antique finishing is optional. DELETE paragraph below if not desired.)

Antique Finish: [Chappo] [Cherry] [Ebony] [Wheat] [White Wash].

(Specifier Note: SELECT desired wood texture below. Smooth texture is standard, Handhewn adds a subtle look of weather-worn waves, Distressed gives an aged, old world appearance and Wire Brushed has rough rustic texture.)

Wood Surface Texture: [Smooth] [Handhewn] [Distressed] [Wire Brushed]

(Specifier Note: Carving is optional. DELETE paragraph below if not desired.)

Door Options: [Carving].

(Specifier Note: Doors are available as prehung or slabs are with hinge and lockset prep. RETAIN one of two paragraphs below.)

Hardware: None. [Prep door for owner supplied hinge and lockset.]

OR

Hardware

Entry Locksets: [Right-hand] [Left-hand]

Exterior escutcheon plate

Key-locking drop bolts

Night latches

[Mortise locks] [Hook latches]

Interior escutcheon plate

Pulls

Style and Finish: Rocky Mountain, [Brushed Stainless Steel][Brushed Bronze].

(Specifier Note: All doors are available prehung with the IWP Insignia( Door System. This package ensures the smoothest installation. It includes all necessary components, including solid hardwood jambs, mouldings, weatherstrip, concealed-bearing hinges and choice of sill types. All components are machined by hand for perfect accuracy. DELETE entire article if not desired.)

PREHUNG HARDWOOD SYSTEMS

Profile

(Specifier Note: Folding door systems are available in several configurations, ranging from two to eight leaves, zero post corners and combination systems. SELECT configuration from list below. DELETE configurations not used.)

Two Door Configuration: [2L] [2R]

Three Door Configuration: [2L1R] [1L2R]

Four Door Configuration: [2L2R] [3L1R] [1L3R]

Five Door Configuration: [4L1R] [1L4R] [3L2R] [2L3R]

Six Door Configuration: [5L1R] [1L5R] [4L2R] [2L4R] [3L3R] [3L3R 90]

Seven Door Configuration: [6L1R] [1L6R] [5L2R] [2L5R] [4L3R] [3L4R]

Eight Door Configuration: [6L2R] [2L6R] [5L3R] [3L5R] [4L4R]

Custom Prehung Options:  [Commercial with ADA-Approved Sill] [Special Mull Post and Pockets] [Oversized] [Direct-set Sidelight Frames]

Jamb

Width: [standard: 4-9/16 inch] [options: [5-1/4 inch] [6-9/16 inch] [7-1/4 inch] [7-1/2 inch] [Custom]].

Profile: [Solid flat] [Rabbeted]

Trim Options:

(Specifier Note: Contact a JELD-WEN® representative to assist in appropriate casing selections or Refer to JELD-WEN® website at www.jeld-wen.com for profiles of casing types listed below.)

Exterior Casing: [#20 Brickmold] [#20 Brickmold w/ Stucco Key] [#21] [#22].

Interior Casing: [#13 Colonial] [#14 Colonial] [#15 Fluted] [#16 Streamlined] [#17] [#23] [#24] [#25] [Custom].

(Specifier Note: Corner Blocks are optional. DELETE if not project specific.)

Corner Blocks: [A (Flower)] [B (Bullseye)] [C (Square)]

Size: [2-1/2 inch square] [2-3/4 inch square] [Custom].

Hinges: Solid brass concealed-bearing.

(Specifier Note: SELECT 4.5 by 4.5 square hinge size below when 2-1/4 inch thick door is specified in fiberglass entrance doors above.)

Size: [4.5 by 4.5 square] [4 by 4 square]

Finish: [Brass] [Chrome] [Oil-Rubbed Bronze] [Satin Nickel]

(Specifier Note: Decorative tips are optional. DELETE paragraph below if not desired.)

Decorative Tips: [Ball] [Urn] [Steeple]

(Specifier Note: Wood sills have no warranty.)

Sills: [Aluminum with [Polished Aluminum] [Polished Nickel] [Brass] [Oil-Rubbed Bronze] Finish] [Wood, [Solid Oak] [Genuine Mahogany]] [No Sill].

(Specifer Note: Various types of glass are available.  The most common types have been included here. All glass styles are not available for all door styles. Contact a JELD-WEN representative to confirm the availability of the desired glazing option or when other options are required.)

GLAZING

Custom: [standard: Tempered, dual glazed] [option: Tempered, single glazed]

Glass Type: [Amethyst Baroque] [Antique Brown] [Antique Clear] [Antique Green] [Antique Light Blue] [Antique Light Purple] [Antique Light Rose] [Antique Medium Amber] [Antique Pale Amber] [Black Baroque] [Blue Baroque] [Cathedral Rose] [Clear Baroque] [Clear Fountain Glass] [Clear Granite] [Clear Krinkle] [Etched/Frosted] [Flash White] [Glue Chip] [Gotta] [Grey Baroque] [Iridescent Granite] [Iridescent Gotta] [Low-E] [Opal Avocado] [Opal Light Green Wispy] [Opal Sense Pale Amber] [Opal Transparent Pale Amber] [Opal Wispy Pale Caramel] [Rain (Cotswald)] [Reed] [Ripple] [Seedy] [Seedy Reamy] [Water Champagne] [Waterglass] [Waterglass Blue] [Waterglass Cherry Red] [Waterglass Light Purple] [Waterglass Pale Amber] [Waterglass Tornasol] [Weave] [Wispy White]

CONSTRUCTION ACCESSORIES

(Specifier Note:  Construction Accessories compatible with doors and required installation may be specified in this section or in related sections.   COORDINATE with related sections to not duplicate information.)

Flashing

Refer to Section [04 20 00 Unit Masonry] [07 60 00 Flashing and Sheet Metal]  [Insert section number and title].

Sealants

Refer to Section [07 92 00 Joint Sealants]  [Insert section number and title].

OR

(Specifier Note:  For sealants specified within this section list recommended products.)

Provide manufacturer recommended sealants maintain watertight conditions.

Products:

[Insert products and manufacturer]

FINISHES

Prefinishing: Permalane prefinishing system uses layers of specially formulated grain filler and UV-protective stain coats which are encapsulated in a final protective top coat.

EXECUTION

GENERAL

Install doors in accordance with manufacturer’s installation guidelines and recommendations.

EXAMINATION

Inspect door prior to installation.

Inspect rough opening for compliance with door manufacturer recommendations. Verify rough opening conditions are within recommended tolerances.

(Specifier Note: DELETE three paragraphs below if prehung system is not specified.)

PREPARATION

Form and install sheet metal sill pan in accordance with manufacturer’s recommendations.

Prepare doors and assemble components for installation in accordance with manufacturer’s recommendations.

INSTALLATION

Insert jamb into rough opening, inspect for good fit, mark location of sill and remove unit.

(Specifier Note: DELETE installation paragraph below if not project specific.)

Insert sidelight into jamb.

Inspect for good fit then remove.

Weatherproof sidelights in accordance with manufacturer’s recommendations.

Insert sidelights back into jamb and tighten jamb to sidelight.

Anchor jamb leg to sidelight through back of rabbeted portion of jamb.

Anchor hinge side mull post to sidelight through hinge.

Anchor strike side mull post to sidelight under lock location.

Anchor top of mull post to sidelight through rabbeted face of jamb.

Anchor bottom of mull post to sidelight through rabbeted portion of mull post.

Prepare door and jamb for installation.

Apply flashing support to backside of sides and head of brickmold.

Apply flashing to corners, backside of frame and brickmold in accordance with manufacturer’s recommendations.

Install jamb over caulk at marked sill location. Check sill for level.

Install jamb assembly.

Shim jambs straight.  Inspect jamb for square, level and plumb.

Fasten jamb to studs.

Structurally secure sill.

Apply sealant to interior side of jamb between outside of jamb and stud to seal gaps.

Install hardware.

Install interior and exterior trim.

Set all nails below surface and fill holes with wood matched putty stick.

Install weatherstrip wedges.

(Specifier Note: DELETE installation paragraph below if not project specific.)

Install transom.

Apply caulk on top of door head jamb.

Set transom jamb on door head jamb and fasten.

Shim transom straight. Inspect transom for square, level and plumb.

Fasten transom to studs.

Insert transom sash.  Inspect for good fit then remove.

Apply caulk along inside corner of transom jamb.

Install transom sash and secure to jamb.

Install interior and exterior trim.

Set all nails below surface and fill holes with wood matched putty stick.

Weatherproofing: Apply in accordance with manufacturer’s recommendations.

PROTECTION

Protect installed doors from damage.

SCHEDULES

(Specifier Note: Below are sample schedules that require editing for specific project.  When a single type of door is utilized on a project, Specifier may elect to delete the schedule in its entirety.  When Schedules are included on the drawings, schedule should be deleted from the specification.)

Door Type A

Basis of Design:	500

Thickness:	1-3/4”

Door Style:	Paneled and Glass

Shape:				Squared Top

Panel Profile:

Divided lites:		One

Panel Mouldings:

Species:	Mahogany

Finish:	Cherry

Finish Options:	None

Surface Texture:	Smooth

Other Options:	None

Hardware:	Right-hand, w/ hook latch, Brushed Bronze finish

Prehung Profile:	3L3R 90

Prehung Options:	None

Jamb Width:	4-9/16 inch

Jamb Profile:	Solid Flat

Exterior Casing:	#21

Interior Casing:	#17

Corner Blocks:	None

Hinges (Size & Finish):	4 by 4, Brass

Decorative Hinge Tips:	Ball

Sill:	Aluminum with Polished Brass

Glazing:	Clear Insulated

Caming:	None

END OF SECTION